## Slide 1
NCR
REALPOS Touch Technology Overview
NCR CONFIDENTIAL
February 18, 2014

## Slide 2
NCR Display Touch Technologies
OVERVIEW
Future Proof - supports 10 point multi-touch/gesturing
Attractive – zero bezel fully flat glass touch surface
Performance – fast & accurate (matrix of rows/columns is “scanned” to calculate precise touch point(s);
More Rugged – glass surface protects electronics, sealed; immune to most chemicals, dust and liquid, can operate in extreme environments; can operate if glass is scratched/damaged; easy to clean
Longest Life – No known wear-out mechanism
Plug “n” Play – No calibration required
Projected Capacitive
Proven Retail Technology - Hundreds of thousand in use
Performance – fast & accurate
Rugged – not affected by dirt, dust, water, or light
Longer Life – 100 million touches (at a single point)
Proven Retail Technology - Hundreds of thousand in use
Best Input Flexibility – finger, glove, stylus, object
Performance – fast & accurate
Rugged - not affected by dirt, dust, water, or light; more immune to operational contaminants - operates with liquid / grease on screen
Long Life - 35 million touches (at a single point)
Attractive – zero bezel fully flat touch surface available (X-Series)
NCR offers touch technologies to meet different retailer requirements
Surface Capacitive
Resistive

## Slide 3
Attribute | NCR Projected Capacitive | NCR Surface Capacitive | NCR Resistive (5 wire) | Infrared (Not used by NCR) | SAW (Not used by NCR)
Technology Description | Capacitive electric grid “projected” thru material below the display glass – Touch measured by detecting change in capacitance of grid | Capacitive electric field on material “surface” – Touch measured by evaluating the capacitance ratio to four corners of the sensor | Membrane coated glass - Touch measured by evaluating the voltage created by the gradient across the sensor and the touch point | Infrared light beams projected above glass in grid – Touch measured by interruption of grid | Surface acoustic waves projected above glass in grid – Touch measured by interruption of grid
Touch capability | Multi-touch (10 point) | Single | Single | Single | Single
Input method | Finger or thin glove | Finger | Finger/Glove/Object | Finger/Glove/Object >.25” | Finger/Glove/Soft Object
Durability (touches at a single point) | No known wear-out mechanism | 225 Million (Mohs 7 - Mineral Hardness Scale) | 35 Million | No known wear mechanism | No known wear-out mechanism
Resistance to environment | Very Good - sealed glass; immune to most chemicals, dust ,liquid, can operate in extreme environments | Very Good - not affected by dirt, dust, water, or light | Excellent – operates with water, grease, on screen | Good - Dirt, Debris, Liquid causes degraded performance or failure | Good - Sensitive to liquid on screen
Resistance to abuse | Continues to operate if scratched or cut | Cut glass causes degraded performance or failure | Lower | High | Scratched or cut glass causes degraded performance or failure
Optical Properties | Excellent | Excellent | Good | Excellent | Very Good
Light Transmissivity | 90% | 86% | 81% | 92% | 90%
Calibration | None | Occasionally (after installation & maintenance) | Occasionally (after installation and maintenance) | None | Occasionally
Immunity to unintended touches | Excellent | Excellent | Excellent | Poor | Excellent
Accuracy | Excellent | Very Good | Very Good | Good | Good
Display Touch Technology
TECHNOLOGY COMPARISON
Notes: Presenter Notes:
NCR P-Cap is compliant not only to Windows 7 but also Windows 8.1. Note that to be Win 8 compliant requires that the touch be able to at least capture 5 point touch. Dual point touch is NOT Win 8.1 compliant (NCR P-Cap is 10 point multi touch)
NCR P-Cap input by glove – note that not all gloves will work. Typically a thin glove or glove with conduct material will work
MoHS is a mineral hardness scale – (~20X greater than 4H)
4H is a hardness scale (#2 pencil is 2H)
Transmissivity – note that a clear pane of glass loses 4% per side of light loss. So, 92% is really the high mark of the scale. (meaning that 86% or even 81% is still very very visible and even difficult to perceive loss)

## Slide 4: Projected Capacitive Touch Technology
Projected Capacitive Description
Projected Capacitive has an electric field grid projected thru materials that are below the display surface glass
Touches are measured by detecting the change in capacitance of the grid.
A matrix of rows/columns is “scanned” to calculate precise touch point(s)
Touch activated by finger or thin glove
Advantages
  Supports multi-touch and gesturing; Windows 7 and 8.1 compliant
  Fast, accurate performance
  Long Life – no known wear-out mechanism
  Zero-bezel fully flat glass touch surface
  Rugged; electronics layers are protected under the sealed glass. Can operate even if glass is scratched or damaged.
  Glass surface is immune to most chemicals, dust, and liquid.
  Operates in extreme environments (Indoor/Outdoor)
  Excellent immunity to unintended touches
  No calibration required
Disadvantages
  Higher cost technology
NCR Product use: RealPOS XR7, X-Series Touch Displays X15-P, X18-P
Note that technology illustrations are of industry technology implementations and do not necessarily represent NCR’s exact implementation.
Typical technology layers in a Projected Capacitive Display.
Typical Projected Capacitive grid patterns.

## Slide 5: Surface Capacitive Touch Technology
Surface Capacitive Description
Surface capacitive has a small electric current field on the surface.
Capacitive sensors at the corners can detect weak current change when touched by something conductive, such as finger.
Advantages
  Long Life – 225M touches at a single point
  Rugged; not affected by dirt, dust, water, or light
  High scratch resistance (Mohs 7 hardness on surface)
  Excellent immunity to unintended touches
  Fast, accurate performance
Disadvantages
  Finger touch only
  Requires occasional calibration
  Does not support multi-touch / gesturing
  Cut glass causes degraded performance or failure
NCR Product use: RP 72XRT, RP50, 5967 Touch, 5954 DynaKey
Typical Surface Capacitive Display.
Note that technology illustrations are of industry technology implementations and do not necessarily represent NCR’s exact implementation.

## Slide 6: Resistive Touch Technology
Resistive Description
Structure includes two layers of ITO coated substrates and micro dots spacers with an air gap. The upper input substrate is made with ITO film or thin ITO glass; the lower substrate is ITO coated film, thick plastic or glass.
When pushing on the upper ITO substrate with a finger or stylus, the two ITO substrates are connected, and the electrical current goes through the point of contact. The controller IC detects and calculates the touch position.
Advantages
  Best Input flexibility – finger/glove/object
  Good immunity to unintentional touches, dirt and liquid
  Operates with liquid or grease on screen
  Fast, accurate performance
  Lower cost technology
Disadvantage
  Does not support multi-touch / gesturing
  Occasional calibration required
  Lower scratch resistance; 3H / 4H hardness on surface
  Lower durability and wear; 35M touches art a single point
NCR Product use: RP 25/50, RP XR7, X-Series X15-R
Typical Resistive Display.
Note that technology illustrations are of industry technology implementations and do not necessarily represent NCR’s exact implementation.

## Slide 7: Surface Acoustic Wave (SAW) Touch Technology
Surface Acoustic Wave (SAW) Description
Surface acoustic wave (SAW) uses a high frequency acoustic wave that is created by the transducers at the corners.
Reflection arrays are used to reflect the acoustic wave to cover the whole surface.
The receivers are used to detect the acoustic signal changes when touched by finger or soft-tip pens.
Advantages
  Very Good Input flexibility – finger/glove/soft object
  Long Life – no known wear-out mechanism
  Good immunity to unintentional touches
  Fast, accurate performance
Disadvantage
  Liquids or condensation can cause false touches
  Low contaminant resistance – surface moisture
  Scratched or cut glass causes degraded performance or failure
NCR Product use: None (low penetration of SAW technology in Retail)
Note that NCR does not currently use Surface Acoustic Wave in its products.
Typical SAW Display.

## Slide 8: Infrared (IR) Touch Technology
Infrared Description
Vertically and horizontally arranged LED lights and detectors are above the display.
Infrared detects the touch position when LED lights are blocked.
There is no overlay on the display surface, so it is mainly used in rugged, public spaces.
Advantages
  Very Good input flexibility – finger / glove / object >.25”
  No calibration required
  Long Life - no known wear-out mechanism
Disadvantages
  Low immunity to objects on the screen
  Low immunity to unintentional touches
  Surface contaminants may create “dead” zones
  Affected by direct sunlight
NCR Product use: None
Typical Infrared Display.
Note that NCR does not currently use Infrared technology in its products.